Tasks:
1. Include Altitude and speed annotations
2. Include Auto pilot annotation
3. Perform auto-pilot control
4. Fix when aruco code is lost from track, the previous cmd vel continues to be transmitted
rosbag record -a

Launching Learning Joy: roslaunch learning_joy turtle_joy.launch

Ref: http://wiki.ros.org/joy/Tutorials/ConfiguringALinuxJoystick

Checking Joystick Input: sudo jstest /dev/input/js0s

Type	Number	Control
Axis	0	Left Thumbstick, left/right
	1	Left Thumbstick, up/down
	2	Right Thumbstick, left/right
	3
	4
	5	Right Thumbstick, up/down
Button	0	Square
	1	Cross
	2	Circle
	3	Trianble
	4	Left/L1
	5	Right/R1

Launching Bebop driver: roslaunch bebop_driver bebop_node.launch

Ref: https://bebop-autonomy.readthedocs.io/en/latest/

Launching Video Reader: roslaunch video_stream_opencv video_file.launch

Note: Play back a video from /learning_joy/sample/output.avi and output as /video_file/image_raw topic.

Launching Image Analysis: roslaunch learning_joy image_analysis.launch

Connecting to Bebop with FTP

Host: 192.168.42.1
Protocol: FTP
Encrpytion: Use plain FTP
Logon Type: Anonymous
Connect.

Update Dependencies:
rosdep update
rosdep install --from-paths src -i

Git:
git add *
git commit -m “text”
git push -u origin master
username: ivanchew92@gmail.com
password: kingdom9419

ROS Topics
/annotated_image/image
/bebop/autoflight/navigate_home
/bebop/autoflight/pause
/bebop/autoflight/start
/bebop/autoflight/stop
/bebop/bebop_driver/parameter_descriptions
/bebop/bebop_driver/parameter_updates
/bebop/camera_control
/bebop/camera_info
/bebop/cmd_vel
/bebop/fix
/bebop/flattrim
/bebop/flip
/bebop/image_raw
/bebop/image_raw/compressed
/bebop/image_raw/compressed/parameter_descriptions
/bebop/image_raw/compressed/parameter_updates
/bebop/image_raw/compressedDepth
/bebop/image_raw/compressedDepth/parameter_descriptions
/bebop/image_raw/compressedDepth/parameter_updates
/bebop/image_raw/theora
/bebop/image_raw/theora/parameter_descriptions
/bebop/image_raw/theora/parameter_updates
/bebop/joint_states
/bebop/land
/bebop/odom
/bebop/record
/bebop/reset
/bebop/set_exposure
/bebop/snapshot
/bebop/states/ardrone3/CameraState/Orientation
/bebop/states/ardrone3/GPSState/NumberOfSatelliteChanged
/bebop/states/ardrone3/MediaStreamingState/VideoEnableChanged
/bebop/states/ardrone3/PilotingState/AltitudeChanged
/bebop/states/ardrone3/PilotingState/AttitudeChanged
/bebop/states/ardrone3/PilotingState/FlatTrimChanged
/bebop/states/ardrone3/PilotingState/FlyingStateChanged
/bebop/states/ardrone3/PilotingState/NavigateHomeStateChanged
/bebop/states/ardrone3/PilotingState/PositionChanged
/bebop/states/ardrone3/PilotingState/SpeedChanged
/bebop/states/common/CommonState/BatteryStateChanged
/bebop/states/common/CommonState/WifiSignalChanged
/bebop/states/common/FlightPlanState/AvailabilityStateChanged
/bebop/states/common/FlightPlanState/ComponentStateListChanged
/bebop/states/common/MavlinkState/MavlinkFilePlayingStateChanged
/bebop/states/common/MavlinkState/MavlinkPlayErrorStateChanged
/bebop/states/common/OverHeatState/OverHeatChanged
/bebop/takeoff
/bebop_joy/autopilot
/bebop_joy/cmd_vel
/bebop_joy/land
/bebop_joy/takeoff
/diagnostics
/joy
/joy/set_feedback
/landing/marker_found
/landing/marker_pose
/rosout
/rosout_agg
/tf
/tf_static

Q1. Is the following param permanent or must it be configured everytime? rosparam set joy_node/dev "/dev/input/jsX"

Q2. How do I make the sourcing permanent?

Cmd: source devel/setup.bash

Ref: http://wiki.ros.org/ROS/Tutorials/InstallingandConfiguringROSEnvironment

Q3. After running the joy_node, the following error message appears, but there doesn’t seem to be any significant impact to the joy stick controls.

slayer9419@slayer9419-XPS-15-9550:~/catkin_ws$ rosrun joy joy_node
[ERROR] [1553789643.492760355]: Couldn't open joystick force feedback!

Q4. No output from video_recorder node.

The file was saved to the /home/.ros folder by default when activated through a launch file. Specify cwd="node" in the node .xml line to specify the output to the current directory. Doesn’t work.

Q5. Unable to compile openCV codes, undefined reference.

Include openCV into the required package line in the Cmake file.

find_package(catkin REQUIRED COMPONENTS
  joy
  roscpp
  turtlesim
  cv_bridge
  image_transport
  OpenCV
)

Q6. xml format for bebop2 flight plan

Ref: https://github.com/mavlink/mavlink/blob/master/message_definitions/v1.0/common.xml
Ref: https://forum.developer.parrot.com/t/create-mavlink-create-panorama-mission-item-and-flight-plan-are-broken-very-weird-results/3184

<entry value="16" name="MAV_CMD_NAV_WAYPOINT">
<description>Navigate to MISSION.</description>
<param index="1">Hold time in decimal seconds. (ignored by fixed wing, time to stay at MISSION for rotary wing)</param>
<param index="2">Acceptance radius in meters (if the sphere with this radius is hit, the MISSION counts as reached)</param>
<param index="3">0 to pass through the WP, if > 0 radius in meters to pass by WP. Positive value for clockwise orbit, negative value for counter-clockwise orbit. Allows trajectory control.</param>
<param index="4">Desired yaw angle at MISSION (rotary wing)</param>
<param index="5">Latitude</param>
<param index="6">Longitude</param>
<param index="7">Altitude</param>

Note 1: Launching Image View Package from Launch File.

Remapping needs to be performed to launch the image_view node through a ROS launch file.

Note 2: Cmd_Vel Timeout

If no piloting command is received by the driver within this timeout period, the driver issues a stop command which causes the drone to hover.

Ref: https://bebop-autonomy.readthedocs.io/en/latest/configuration.html

To solve the problem, create a node that publishes at a fix rate to avoid the timeout problem.

Note 3: Creating bounding box from contours objects

Ref: https://docs.opencv.org/2.4.13.7/doc/tutorials/imgproc/shapedescriptors/bounding_rects_circles/bounding_rects_circles.html

Note 4: Performing Multi-Object Tracking

Ref: https://www.learnopencv.com/multitracker-multiple-object-tracking-using-opencv-c-python/

Error:

/home/cerc/catkin_ws/src/light_inspector/src/tracking_test.cpp: In function ‘cv::Ptr<cv::Tracker> createTrackerByName(std::__cxx11::string)’: / /home/cerc/catkin_ws/src/light_inspector/src/tracking_test.cpp:58:19: error: ‘cv::TrackerCSRT’ has not been declared / tracker = cv::TrackerCSRT::create();

- Image tracking functions in quite an unusual manner.

Note 5: Other Useful Projects

Similar application concept to light inspector: https://github.com/TOTON95/Bebop_ROS_Examples

Technical specification for regulators: https://forum.developer.parrot.com/t/bebop2-systems-manual/6722/2

SAFETY NOTE: Axis numbers for the PS4 controller changed when another machine was used. Prior to using the package, it is important to verify that the axis corresponds with the desired buttons.

SAFETY NOTE: In the case where link is loss between drone and computer, the RH route would be activated and the drone would climb, proceed to the take-off x,y coordinates and descend to a holding mode. Thereafter, de-link the wifi connection and re-connect. Re-launch the node and land the drone.
USEFUL CODE SNIPPETS

Function: Get openCV Mat image center

cv::Point image_center; / image_center.x = image_tracker.cols/2; / image_center.y = image_tracker.rows/2; / cv::circle(image_tracker, image_center, 5, color_red, 5, 8, 0); / ROS_DEBUG_STREAM("Image Center " << image_center);